Section 1 : PRODUCT AND COMPANY IDENTIFICATION Product name: Nitrogen (Gaseous), Supplier/ Manufacturer: Star special air gases pvt.ltd Plot no.324,sector 7,phase2 IMT,Gurgaon,Manesar India Phone:0124-4368121/. 23/25/30

Section 2 : COMPOSITION/ INGREDIENT INFORMATION C.A.S. CONCENTRATION % Ingredient Name OSHA PEL ACGIH TLV OSHA STEL 7727-37-9 > 99 NITROGEN NONE SIMPLE ASPHYXIANT NONE

Section 3 : HAZARD IDENTIFICATION Emergency Overview: Nitrogen gas is colorless, odorless and non-flammable. It is non-toxic. The primary health hazard is asphyxiation by displacement of oxygen. Route of entry: Inhalation, skin and eye contact. Effects of acute exposure Eye contact: Vapor may cause a stinging sensation. Skin contact: No adverse effects from gas. Inhalation: May cause dizziness. Asphyxiant. Can cause vomiting. May result in unconsciousness. May cause excitation, excess salivation, rapid breathing. May cause headaches and drowsiness. May cause stinging of the nose and throat. Ingestion: Not a likely route of exposure. Effects of chronic exposure: None known. Chronic exposure to abnormal concentrations unlikely Reproductive effects: Oxygen deficiency during pregnancy has produced developmental abnormalities in humans and experimental animals.

Section 4 : FIRST AID MEASURES Skin contact: None required. Eye contact: None required. Inhalation: RESCUERS SHOULD NOT ATTEMPT TO RETRIEVE VICTIMS OF EXPOSURE TO THIS PRODUCT WITHOUT ADEQUATE PERSONAL PROTECTIVE EQUIPMENT. At a minimum, Self-Contained Breathing Apparatus should be worn. Remove victim(s) to fresh air, as quickly as possible. If not breathing qualified personnel should administer artificial respiration. Get medical attention. If breathing is difficult, administer oxygen. Ingestion: No first aid should be needed. Not considered a potential route of exposure.

Section 5 : FIRE FIGHTING MEASURES Flammability: Not flammable. Conditions of flammability: Will not burn. Extinguishing media: Use appropriate extinguishing media for surrounding fire. Special procedures: Self-contained breathing apparatus required. Firefighters should wear the usual protective gear. Cool fire exposed containers with water spray. Personnel should be evacuated, if necessary, to upwind area. Remove containers from fire area if without risk. Auto-ignition temperature: Not applicable. Flash point (°C), method: Not applicable. Lower flammability limit (% vol): Not applicable. Upper flammability limit (% vol): Not applicable. Explosion Data Sensitivity to mechanical impact: Avoid impact against container. Explosive power: Closed containers may rupture or explode due to pressure build-up when exposed to extreme heat. Cylinders are equipped with temperature and pressure relief devices but may still rupture under fire conditions.

Section 6 : ACCIDENTAL RELEASE MEASURES Leak/Spill: Evacuate all non-essential personnel. Stop leak without risk. Wear gloves and goggles Use a self-contained breathing apparatus. Ventilate area. Monitor the surrounding area for Oxygen level. Oxygen must be at least 19.5% before personnel may be allowed into the area without self-contained breathing apparatus. If the area must be entered by emergency personnel, self-contained breathing apparatus, Kevlar gloves, and appropriate foot and leg protection must be worn.

Section 7 : HANDLING AND STORAGE Handling procedures and equipment: Protect system components against physical damage. Use adequate ventilation. Avoid inhalation. Never work on a pressurized system. If there is a leak, close the upstream valve, blow down the system by venting to a safe place, then repair the leak. Storage requirements: Use storage containers, piping, valves and fittings designed for storage and distribution of Gaseous Nitrogen. Protect cylinders against physical damage. Store in cool, dry, well-ventilated, fireproof area, away from flammable materials and corrosive atmospheres. Store away from heat and ignition sources and out of direct sunlight. Do not store near elevators, corridors or loading docks. Do not allow area where cylinders are stored to exceed 52°C (125°F). Move cylinders with a suitable hand-truck. Do not drag, slide or roll cylinders. Do not drop cylinders or permit them to strike each other. Secure cylinders firmly. Leave the valve protection cap in-place (where provided) until cylinder is placed into service and after it is taken out of service. Use designated CGA fittings and other support equipment. Do not use adapters. Do not heat cylinder by any means to increase the discharge rate of the product from the cylinder. Use check valve or trap in discharge line to prevent hazardous backflow into the cylinder. Do not use oils or grease on gas-handling fittings or equipment. After use, close main cylinder valve. Replace valve protection cap (where provided). Mark empty cylinders "EMPTY".

Section 8 : EXPOSURE CONTROLS / PERSONAL PROTECTION Precautionary Measures Gloves/Type: Work gloves Respiratory/Type: NIOSH/MSHA approved respirator. Eye/Type: As per local regulations. Footwear/Type: Safety boots per local regulations. Clothing/Type: Wear adequate protective clothes. Other/Type: Eye wash facility should be in close proximity. Emergency shower should be in close proximity. Ventilation requirements: Mechanical ventilation is satisfactory. Ensure oxygen concentration remains above 19.5% and Carbon Dioxide concentration does not exceed 5000 ppm, Local exhaust at points of emission preferred. Exposure limit of material Simple asphyxiant.

Section 9 : PHYSICAL AND CHEMICAL PROPERTIES Physical state: Gas Appearance & odor: Colorless, odorless gas. Odor threshold (PPM): Odorless. Vapor pressure : Gas@ 70°F (21°C) Vapor sp. gravity (air=1): 0.967 @ 70°F (21°C) Volatiles (% by volume) 100% Boiling point : -195.8°C (760 mmHg) -320.4°F Freezing point : -209.9°C -345.8°F Solubility in water (%): Slight.

Section 10 : STABILITY AND REACTIVITY Chemical stability: Product is stable. Conditions of reactivity: Heat Hazardous polymerization: Will not occur. Incompatible substances: Lithium. Titanium. Neodymium. Hazardous decomposition products: None.

Section 11 : TOXICOLOGICAL INFORMATION LD50 of product, species & route: Not available. LC50 of product, species & route: Not available.

Section 13 : DISPOSAL CONSIDERATIONS Waste disposal: Gas will dissipate in air. Cylinders should be returned in the original shipping container, properly labeled, with any valve outlet plugs or caps secured and valve protection cap in place.

Section 14 : TRANSPORT INFORMATION DOT/ TDG classification: : For cylinder shipments: Nitrogen, compressed UN 1066 DOT Class 2.2 (Non-Flammable Gas)

Section 15 : REGULATORY INFORMATION WHMIS classification: A DSL status: Appears on DSL.

Section 16 : OTHER INFORMATION

USE OF THIS INFORMATION: Star Special Air Gases, offers this information to customers, employees, contractors, and the general public to promote the safe use of this product through awareness of product hazards and safety information. Customers and others who use or transport or sell this product to others should: 1) Disseminate this information internally to all workplace areas, employees, agents and contractors likely to encounter this product; 2) Provide supplemental hazards awareness, safety information, operation and maintenance procedures to the workplace areas and employees, agents and contractors likely to encounter this product; 3) Furnish this information to all their customers who purchase this product; and 4) Ask each purchaser or user of the product to notify its employees and customers of the product hazards and safety information.

DISCLAIMER OF EXPRESSED AND IMPLIED WARRANTIES: Star special air gases, I has taken reasonable care in preparing this document, however, since the use of this information and the conditions of use of the product are not within the control of Star Special Air Gases, it is the user's obligation to determine the conditions of safe use of this product. The information in this document is offered with no warranties or representations as to accuracy or completeness and it is the responsibility of each individual to determine the suitability of the information for their particular purpose(s).